# Manual for EC_NCDF (version 2.5.23.1.3)

## Introduction
This document describes the use of ec_ncdf, a program to process eddy-covariance data stored in NetCDF files. ec_ncdf is built on top of a library of functions, ecpack.
Ecpack and ec_ncdf were intially developped by Arjan van Dijk, and now maintained and further developped by Arnold Moene (arnold.moene@wur.nl). The development was initiated as the result of a special interest group composed of Henk de Bruin (then WUR), Cor Jacobs (then KNMI), Arjan van Dijk (then WUR), Wim Kohsiek (then KNMI), Fred Bosveld (KNMI) and Bart van de Hurk. The aim of the special interest group was to develop a standard processing method for eddycorrelation data. With such a standard method results will become better comparable.
Ecpack is released under the GNU Public License.

In case you use our software in a publication, please acknowledge our work by citing: Van Dijk, A., Moene, A.F., and De Bruin, H.A.R., 2004: The principles of surface flux physics: theory, practice and description of the ECPACK library, Internal Report 2004/1, Meteorology and Air Quality Group,
Wageningen University, Wageningen, the Netherlands, 99 pp.

DISCLAIMER/COPYRIGHT: Ecpack is released under the GNU Public License.
Furthermore: EC-Pack is provided as is. No responsibility can be taken for consequences of the use of EC-Pack. Any use of EC-Pack is done at your own risk.

## Usage
The program is controlled by a large number of configuration files (we are in the process of reducing this number).

The program is invoked as:
ec_ncdf < configfile

where configfile is the name of the main configuration file of which the structure is described below. Thus the configuration is read from standard input. If you would like to write the output produced by ec_ncdf to a file (e.g. to check for error messages) you can redirect the output to a file:
ec_ncdf < configfile > outputfile

If you want to append output to an already existing outputfile, you can do:
ec_ncdf < configfile >> outputfile

### Configuration file
The configuration contains one assignment per line. A known issue is that the file should NOT end with an empty line.
Comments are allowed in any line. Recognized commenting characters are either a hash (#) or a double slash (//). All characters right of the leftmost commenting character in each line are ignored.

Assignments are of the form
 VARNAME = VALUE

where VARNAME is one of a prescribed list of tokens and VALUE is the value to be assigned (VALUE may be placed between quotes, but this is not necessary as long as no spcaes are part of VALUE). VARNAME is case-insensitive (i.e. VARNAME is equivalent to VarName), but VALUE may not be (on UNIX path names are cases sensitive and names of variables in a NetCDF file are also cases-sensitive).
As of version 2.5, one can control, through the main configuration file, which data are written to the output file

The main configuration file can contains data file information, processing parameters and calibration data. There are two modes to store such information
- one configuration file
- separate configuration files

In the first case, all tokens and comments are defined in one file. In the second case, one or more parts of the information can be stored in separate files of the same format. Such files have to be specified in the configuration file using the token "Include". Included files are processed at the position in the configuration file, where they are included. The "Include" token must not be used in included files. Note that in case of multiple occurrences of a token (except "Include") only the last assignment is used. This allows e.g. to store your personal defaults in a file and then change only a few assignments by overwriting the included assignments below in the configuration file.

The traditional configuration stored in multiple files of different format is still supported, too (see next Section 2.2 on page 9)

Note that the names of the data files as well as of the intermediate results files are to be specified in the
interval file (see Section 2.3, page 12) rather than in the configuration file.

Figure 1: Filename specification. An arrow means that the file from which the arrow points contains the name of the file pointed to.

Intermediate results file
Data file

Interval file
Flux output file
Configuration file
#### Data file information
Valid tokens (variable names) are:
DatDir	directory for data files
OutDir	directory for output files (flux files, intermediate result file)
ParmDir	directory for parameter files
Include	include the given file from directory ParmDir
FluxName	name of flux output file
InterName	name of interval file
PlfIntName	name of file that defines the intervals over which planarfit angles should be calculated
PlfName	name of file to which the planar fit angles should be written
U_var	name of u-velocity variable in NetCDF file
V_var	name of v-velocity variable in NetCDF file
W_var	name of w-velocity variable in NetCDF file
TSonic_var	name of sonic temperature variable in NetCDF file
SSpeed_var	name of speed of sound variable in NetCDF file (used to compute TSonic if the latter is not available in the NetCDF file)
TCouple_var	name of thermocouple temperature variable in NetCDF file
Tref_var	name of thermocouple reference temperature variable in NetCDF file
Humidity_var	name of humidity variable in NetCDF file (H2O concentration should be in kg/m3 or the calibration file should take care of that)
CO2_var	name of CO2 variables (CO2 concentration should be in kg/m3 or the calibration file should take care of that
HourMin_var	name of hour/minute variable in NetCDF file (presently this should be a la the Campbell hour/minutes: e.g. 1845 means 18:45
Doy_var	name of day of year variable in NetCDF file
sec_var	name of seconds variable in NetCDF
Out_mean	write mean of given calibrated signal to output file (e.g. Out_mean='TSon', for a list of variable names, see below)
Out_Cov	write covariance of two calibrated signal to output file (e.g. Out_Cov='TSon,w', for a list of variable names, see below)
Out_Std	write standard deviation of given calibrated signal to output file (e.g. Out_Std='TSon', for a list of variable names, see below)
Out_Num	write number of samples of given calibrated signal to output file (e.g. Out_Num='TSon', for a list of variable names, see below)
Out_Phys	write given physical (=derived quantity) to output file (e.g. Out_Phys='HSonic', for a list of variable names, see below)
Out_Time	write some extra time columns regarding start and stop of interval: e.g. Out_Time='DecHourB' / DecDayB: starttime in decimal days (starting on January 1) / DecDayE: stoptime in decimal days (starting on January 1) / DecHourB: startttime in decimal hours (starting at midnight) / DecHourE: stoptime in decimal hours (starting at midnight) / DecSecB: startttime in decimal seconds (starting at midnight) / DecSecE: stoptime in decimal seconds (starting at midnight)
Out_Struct	write (cross-) structure paramter of two calibrated signals to output file (e.g. Out_Struct='TSon,w', for a list of variable names, see below). Note that for the moment if you request structure paramters through Out-Struct, you still have to specify DoStruct = .T. in the processing paramters file (see below).
Output	other output settings: / 'new': use new output file format (i.e. with self-defined columns / 'old': use old output file format (pre-defined columns; 'new' and 'old' are mutually exclusive; 'old' is default (defined in ec_ncdf.f)) / 'csv': output as comma-separated values / 'ssv': output as space-separated values ('csv' and 'ssv' are mutually exclusive; 'ssv' is default) / 'tol': write tolerances of all selected variabels to output file / 'notol': write no tolerances of all selected variabels to output file ('tol' and 'notol' are mutually exclusive; 'tol' is default) / 'diag': write info about diagnostic flags of CSAT to output file / 'nodiag': write no info about diagnostic flags of CSAT to output file ('diag' and 'nodiag' are mutually exclusive; 'nodiag' is default) / 'version': write version number of software to output file / 'noversion': write no version number to output file ('version' and 'noversion' are mutually exclusive; 'version' is default)
correct	switch for corrections. These switches will have the same functionality as the booleans read from the parameter file called ParmName. In the end this structure will replace the use of the parameter file (since the latter is not flexible enough), but currently the parameter file is still needed. / The structure of the rigth hand side of the switch is: / 'NAME : ONOFF', where NAME is the name of the correction and ONOFF is either ON or OFF / Valid names for the corrections are: / 'detrend' : Correct data for linear trend / 'tilt' : Perform true tilt-correction with known angles / 'yaw' : Turn system such that Mean(V) --> 0 / 'pitch' : Turn system such that Mean(W) --> 0 / 'roll' : Turn System such that Cov(W,V) --> 0 / 'planfit' : Do planar fit untilting (requires that untilting angles have been produced before with planang) / 'sontemp' : Correct sonic temperature for humidity / 'oxygen' : Correct hygrometer for oxygen-sensitivity / 'freqresp': Correct for poor frequency response / 'webb' : Calculate mean velocity according to Webb / 'slowmean': Replace mean quantities by better estimates (currently only humidity) / 'blockav' : detrend by block averaging, rather than linear detrending
corrpar	switch to pass parameters needed in corrections. Structure of right hand side is: / 'NAME : VALUE', where NAME is the name of the parameter and VALUE is its value / Valid names at this moment are: / 'Nblock' : number of blocks into which the averaging interval should be divided when doing block averaging

Variable names to be used for Out_Mean, Out_Cov, Out_Std, Out_Struct (defined in parcnst.inc, not case-sensitive):
u	horizontal wind component [m/s]
v	horizontal wind component [m/s]
w	vertical wind component [m/s]
TSon	sonic temperature [K]
TCop	thermocouple temperature [K]
rhoV	water vapour density' [kg m^-3]
q	specific humdity [kg/kg]
rhoCO2	CO2 density [kg m^-3]
qCO2	specific CO2 concentration [kg/kg]
time	time (constructed from DOY, Hour and Min) [hr]
Tref	reference temperature [K]
all	select all defined variables (e.g. Out_Cov='w,all' gives all covariances with the vertical velocity, Out_mean='all' gives means of all variables)

Variable names to be used for Out_Phys (defined in parcnst.inc, not case-sensitive):
RhoSon	air density with sonic temperature[kg/m^3]
RhoTc	air density with thermocouple [kg/m^3]
Wnorot	vertical wind speed before any axis rotation [m/s]
U_Vect	(was VectWind, still works) vector wind [m/s]
U_dir	(was DirFrom, still works) wind direction [degr.]
HSonic	sensible heat flux from sonic temperature [W/m^2]
HTc	sensible heat flux from thermocouple[W/m^2]
LvEcov	covariance LvE [W/m^2]
LvEWebb	Webb term LvE [W/m^2]
SumLvE	sum of LvEcov and LvEWebb [W/m^2]
Ustar	u* [m/s]
Tau	wall shear stress [N/m^2]
FCO2cov	covariance CO2 flux [kg/m^2/s]
FCO2Webb	Webb term CO2 flux [kg/m^2/s]
SumFCO2	sum of covariance and Webb CO2 flux [kg/m^2/s]
all	gives all defined physical quantities

#### Processing parameters
Tokens indicating the desired way of processing are of the form "Par.<Specifiers>". If any of the specifiers is not defined, the default value displayed in the third column will be used. Valid specifiers are:
FREQ	Sample frequency of datalogger in Hz	20
YawLim	Limit when Mean(W) is turned to zero in degrees	30
RollLim	Limit when Cov(V,W) is turned to zero in degrees	30
PreYaw	Fixed pitch angle for known tilt-correction in degrees	0
PrePitch	Fixed yaw angle for known tilt-correction in degrees	0
PreRoll	Fixed roll angle for known tilt-correction in degrees	0
LLimit	Smallest acceptable freq-response corr. factor	0.85
ULimit	Largest acceptable freq-response corr. factor	1.15
DoCrMean	Replace mean quantities by better estimates	T
DoDetrend	Correct data for linear trend	T
DoSonic	Correct sonic temperature for humidity	T
DoTilt	Perform true tilt-correction with known angles	F
DoYaw	Turn system such that Mean(V) --> 0	T
DoPitch	Turn system such that Mean(W) --> 0	T
DoRoll	Turn System such that Cov(W,V) --> 0	T
DoFreq	Correct for poor frequency response	T
DoO2	Correct hygrometer for oxygen-sensitivity	T
DoWebb	Calculate mean velocity according to Webb	T
DoIterate	Iterate interdependent corrections	F
MaxIter	Maximum number of such iterations	5
DoStruct	Calculate structure coefficients	T
StructSep	separation (in m) used for calculation of structure parameters	0.15
DoPF	Do planar fit untilting	T
PFValid	Fraction of valid samples required to include interval in planar fit	0.99
DoPrint	Skip printing intermediate results or not?	F
PRaw	Indicator if these intermediate results are wanted	T
PCal	Indicator if these intermediate results are wanted	T
PDetrend	Indicator if these intermediate results are wanted	T
PIndep	Indicator if these intermediate results are wanted	T
PTilt	Indicator if these intermediate results are wanted	T
PYaw	Indicator if these intermediate results are wanted	T
PPitch	Indicator if these intermediate results are wanted	T
PRoll	Indicator if these intermediate results are wanted	T
PSonic	Indicator if these intermediate results are wanted	T
PO2	Indicator if these intermediate results are wanted	T
PFreq	Indicator if these intermediate results are wanted	T
PWebb	Indicator if these intermediate results are wanted	T
PPF	Print intermediate results after planar fit untilting	T

#### Calibration information
Tokens indication calibration information are of the form "<Prefix>.<Specifiers>". With each prefix, all tokens need to be specified. There are no defaults, hence not defining all necessary specifiers will result in abort.

Valid prefixes are:
SonCal	sonic calibration
CoupCal	thermo couple calibration
HygCal	hygrometer calibration
CO2Cal	CO2 sensor calibration

Valid specifiers are:
QQType	now 12 types of sensors are known: / Campbell Sonic (30 degree angle with vertical) / thermo couple (undefined type) / Krypton hygrometer / PT100 thermometer / Psychrometer (used for what?) / wind tunnel calibrated sonic anemometer / Mierij Lymann-alpha / LiCor7500 IR H20/CO2 sensor / Kaijo Denki TR90 3-D sonic / Kaijo Denki TR61 3-D sonic / Gill Solent anomemeter (45 degree angle with vertical, wind direction might still be incorrect: not tested) / Generic sonic (specfici parameter are passed as extra calibration coefficients)
QQX, QQY, QQZ	are used for frequency response corrections (note that the height is an absolute height above the surface (or better: above the displacement height)
QQFunc	Two types of fit functions are available / Polynomial / logarithmic polynomial
QQExt1 to QQExt5	These are used to specify calibration factors specific to a type of sensor . For QQType = 6, six extra calibration factors are available (QQExt6 to QQExt11) to define the wind tunnel calibration; see Wind tunnel calibrated sonic). / For the generic sonic (QQType = 12) five extra additional calibration coefficients are defined (see Generic Sonic)

The gain and offset are used for all apparatuses (it is done directly after reading the samples). The calibration curve is presently only used for the thermocouple (QQType = 2), hygrometer (i.e. QQType is 3, 7 or 8) and the CO2 signal (QQType = 8). Make sure that -at least for those apparatuses where the calibration curve is used- you enter sensible values for QQFunc, QQC0, QQC1 and QQOrder (for just a one-to-one conversion, enter 1, 0, 1 and 1, respectively).

See section on Program internals on how gain, offset and calibration polynomials are treated.

### Traditional Multi-file Configuration
Figure 2: Hierarchy of traditional configuration files (an arrow means that the file from which the arrow points contains the name of the file pointed to)

Intermediate results file
Data file

Calibration files
Flux output file
Interval file
Processing parameter file
Main configuration file

The hierarchy of configuration files is shown in Figure 2 (an arrow means that the file from which the arrow points contains the name of the file pointed to).

#### Main configuration
Additional tokens (variable names) to specify the traditional-style additional configuration files are:
ParmName	name of processing parameter file
SonName	name of sonic calibration file
CoupName	name of thermo couple calibration file
HygName	name of hygrometer calibration file
CO2Name	name of CO2 sensor calibration file

Valid tokens in the main configuration file are (for definition see Section 2.1.1 on page 3):
Directories:
DatDir, OutDir, ParmDir
File names:
FluxName, InterName, PlfIntName, PlfName
Variable names:
U_var, V_var, W_var, TSonic_var, SSpeed_var, TCouple_var, Tref_var, Humidity_var, CO2_var, HourMin_var, Doy_var, sec_var
Output specification:
Out_mean, Out_Cov, Out_Std, Out_Num, Out_Phys, Out_Time, Out_Struct, Output, correct, corrpar
Variable names to be used for Out_Mean, Out_Cov, Out_Std, Out_Struct (defined in parcnst.inc, not case-sensitive):
u, v, w, TSon, TCop, rhoV, q, rhoCO2, qCO2 , time, Tref, all
Variable names to be used for Out_Phys (defined in parcnst.inc, not case-sensitive):
RhoSon, RhoTc , Wnorot, U_Vect, U_dir, HSonic, HTc, LvEcov, LvEWebb, SumLvE, Ustar, Tau, FCO2cov, FCO2Webb, SumFCO2, all
#### Processing parameter file
The parameter file contains information on how to process the data. The information is expected on fixed line, so blank lines are significant! At the moment parameter file consists of seven blocks:
1. sample frequency
2. limits on yaw and roll correction
3. fixed ptch, yaw and roll angles
4. limits on frequency response corrections factors
5. 'corrections' to perform
6. switch for yes/no printing of intermediate results
7. switches for which intermediate results to print

20	FREQ	= ! [Hz] Sample frequency datalogger

30	YawLim	= ! [degree] Limit when Mean(W) is turned to zero
30	RollLim = ! [degree] Limit when Cov(V,W) is turned to zero

0	PreYaw = Fixed pitch angle for known tilt-correction
0	PrePitch = Fixed yaw angle for known tilt-correction
0	PreRoll = Fixed roll angle for known tilt-correction

0.85	LLimit	= ! Smallest acceptable freq-response corr. factor
1.15	ULimit	= ! Largest acceptable freq-response corr. factor

T	DoCrMean = ! Replace mean quantities by better estimates
T	DoDetren = ! Correct data for linear trend
T	DoSonic = ! Correct sonic temperature for humidity
F	DoTilt	= ! Perform true tilt-correction with known angles
T	DoYaw = ! Turn system such that Mean(V) --> 0
T	DoPitch	= ! Turn system such that Mean(W) --> 0
T	DoRoll	= ! Turn System such that Cov(W,V) --> 0
T	DoFreq	= ! Correct for poor frequency response
T	DoO2	= ! Correct hygrometer for oxygen-sensitivity
T	DoWebb	= ! Calculate mean velocity according to Webb
T	DoStruct = ! Calculate structure coefficients

F	DoPrint = ! Skip printing intermediate results or not?

T	PRaw	= Indicator if these intermediate results are wanted
T	PCal	= Indicator if these intermediate results are wanted
T	PDetrend = Indicator if these intermediate results are wanted
T	PIndep	= Indicator if these intermediate results are wanted
T	PTilt	= Indicator if these intermediate results are wanted
T	PYaw	= Indicator if these intermediate results are wanted
T	PPitch	= Indicator if these intermediate results are wanted
T	PRoll	= Indicator if these intermediate results are wanted
T	PSonic	= Indicator if these intermediate results are wanted
T	PO2	= Indicator if these intermediate results are wanted
T	PFreq	= Indicator if these intermediate results are wanted
T	PWebb	= Indicator if these intermediate results are wanted
0.15	StructSep = separation (in m) used for calculation of structure parameters
T	DoPF = Do planar fit untilting (produce angles before with planang)
T	PPF = Print intermediate results after planar fit untilting
0.99	PFValid = Fraction of valid samples required to include interval in planar fit
Figure 3: Example of parameter file
In Figure 3 you will find an example of a parameter file.I f you use planar fit untilting, the 'classic' axis rotation should be switched off (using both planar fit and 'classic' doesn't make sense, since in
the end you would only see the effect of the 'classic ' method. However, the planar fit method does not turn the system into the mean wind. Therefore, it is practical to keep the Yaw correction switched on.
This will ensure that mean(v) becomes zero (please refer to the definition of the specfile given above to find the correct line where the Yaw correction is switched on or off, there has been confusion about what is Yaw and what is pitch: spec files that are copies of copies of copies of old spec files might have the wrong naming!
#### Calibration files
The structure of the calibration files is identical for all sensors. The file consists of 27 lines (for most sensors), with one number per line. The order of the lines is significant and no blank lines should be present.
An example of a calibration file is given in Figure 4. For the explanation of the parameters see 2.1.3 an page 7
1	QQType ! Either of the ApXXXXXX numbers
296	QQIdent ! True series-number of the apparatus
1	QQGain ! Gain in this experiment
0	QQOffset ! Offset in this experiment
0	QQX	! Absolute x-position of the focal point
0	QQY	! Absolute y-position of the focal point
3.52	QQZ	! [m] Absolute z-position of the focal point
0	QQC0	! Zeroth order coefficient of calibration
1	QQC1	! First order coefficient of calibration
0	QQC2	! Second order coefficient of calibration
0	QQC3	! Third order coefficient of calibration
0	QQC4	! Fourth order coefficient of calibration
0	QQC5	! Fifth order coefficient of calibration
0	QQC6	! Sixth order coefficient of calibration
287	QQYaw ! [degree] Yaw angle of apparatus relative to north
0	QQPitch ! Pitch angle
0	QQRoll ! Roll angle
1	QQOrder ! Order of the calibration model
1	QQFunc ! Type of fitfunction
0.1	QQPath ! [m] Path length over which sensor integrates
0	QQTime ! Time constant
0	QQDelay ! [ms] Delay of this apparatus
0	QQExt1 ! Factor for conversion of sonic temperature signal
1	QQExt2 ! Multiplication factor for sonic temperature due to path length
0.1	QQExt3 ! [m] distance w-u
0.1	QQExt4 ! [m] path length sonic T
0	QQExt5 ! Additional calibration coefficient
Figure 4: Example calibration file
Note that sometimes on Windows machines the program fails to read the last line of the calibration file (due a difference in text file format between Unix and Windows). In that case it helps to add an empty line at the end of the calibration file.

### Interval file
The interval file describes for which times intervals fluxes have to be computed from which data files etc. The format is:
- one blank line (can be used for a heading, comments ...)
- one line per interval, where the interval is described with the following columns:
1. Starting day of year number
2. Starting hour
3. Starting minutes
4. End day of year number
5. End hour
6. End minutes
7. Water vapour density (in kg/m3) from a slow sensor (used to correct for drift of the fast hygrometer)
8. Atmopheric pressure (in Pa)
9. Name of data file
10. Name of file for intermediate results

Note that the program determines the time interval such that the datapoint should have a time that corresponds a doy,hour,minute combination within the interval specified, including the start time, but excluding the end time This implies that e.g. the interval 255 13 00 255 13 30 corresponds to all samples between (inclusive) 255,13:00:00 and 255,13:30:00 (this different from the behaviour before version …).

### Data file
A NetCDF file. The file is searched for the variables specified in the main configuration file. All attributes to variables are ignored (including units) except for 'scale_factor' and 'add_offset'. How these are treated in combination with gain and offset and calibration read from the calibration file is treated in the section on Program internals.
The variables in the file, or the variables in combination with the various gain and offsets (in NetCDF file or calibration file) and the calibration curve given in the calibration file should have
the following units:

U	m/s
V	m/s
W	m/s
TSonic	Celcius (since there is no easy way to convert the sonic temperature in the calibration file; anyhow, degree Celcius is a permitted SI unit)
TCouple	Celcius (to remain compatible with the sonic temperature)
rhov	kg/m3 (was g/m3, until Sept 18, 2002)
rhoCO2	kg/m3 (was g/m3, until Sept 18, 2002)
Tref	Celcius (a compromise, since there is no calibration file for the reference temperature it's not easy to change it's units)

The time in the file is supposed to be in the terrific Campbell HHMM format.

### Intermediate results file
A (possibly huge) text file that gives information on a variety ofthings:
- data file from which data where read
- time interval
- time scales
- all (cross-correlations) between calibrated variables
- the latter can be shown after each correction/operation on the data
For each time interval this file is started again (so if you want to store intermediate results from more than one time interval, they shouldhave different neames for each time interval; this is defined in
the interval file).

### Flux output file
The flux output file contains one line per interval, stating the number of samples read, means, variances and covariances of variables as well as the tolerances of those quantities. A header line explains the contents.
For each complete run of the program (comprising various time intervalsas defined in the interval file) the data are appended.
One can either use a predefined set of columns (set Output='old' in the main configuration file) or defined the required columnsyourselve (set Output='new' and define the columns in the
main configuration file).
Note that although the contents of the flux output file is now configurable, the order of the columns is fixed (i.e. independent of the order in which output is requested in the configuration file). The order of the blocks of output is (since version 2.5.7):
- time columns (always)
- # samples (always)
- # samples per variable (on request)
- diagnostics (on request)
- means (on request)
- standard deviations (on request)
- covariances (on request)
- structure parameters (on request)
- physical parameters (incl. fluxes) (on request)

Within the block of physical parameters, the fluxes come last.

## Program internals
A number of details on the internal operation of the program will be
discussed here.

### Gain, offset etc.
The order in which the various gains, offsets and calibrations are applied to the data is as follows:
- if scale_factor present: sample = sample * scale_factor
- if add_offset present: sample = sample + add_offset
- gain from calibration file: sample = sample / gain
- offset from calibration file: sample = sample + offset
- calibrtion curve : sample = calibration_function(sample)

### Frequency response correction
Due to lack of information on the cospectra of u and v with scalars and of different scalars, the frequency respsonse correction is only applied to variances and to covariances of scalars with
the vertical velocity w. Currently no information is used on the exact arrangement of the sonic tranducers.

## Details on specific sensors
### Thermo couple
If no name for a reference temperature variable is given in the main configuration file (i.e. Tref_var is empty) it is assumed that the variabele Tcouple_var contains the temperature itself (in deg Celsius)
If a reference temperature is given, it is assumed that the variables Tcouple_var contains a voltage, which is the voltage between the actual sensor and the reference junction. The temperature is then
determined as:
T = f(voltage + f-1(reference T))
where f is the calibration function given in the calibration file, and f-1 is the inverse of the calibration function. It is assumed that the calibration function yields a temperature in degrees Celsius. The reference temperature is also supposed to be in degrees Celcius.

This procedure is in accordance with what is done in the P14 instruction of the Campbell dataloggers.

### Krypton hygrometer
The calibration of the Krypton hygrometer as given in the manual of the instrument is not really compatible with the way in which calibrations are treated in the present program. According to the Krypton manual the calibration is:
ln(V) = ln(V0) - rho x K
where V is the output voltage, V0 is the voltage in absence of water vapour, x is the path length and K is the effective extinction coefficient. In order to convert this calibration to a (log) polynomial, the calibration curve has to be fitted to either model. This implies that when the path length is changed, a new calibration curve needs to be fitted (of course no recalibration needed). To cope with the 'wet' calibration and 'dry' calibration as suggested by Campbell a second order log-polynomial can be
used.

### LiCor 7500 IR hygrometer / CO2 sensor
You have a variety of choices in the output of this sensor. ec_ncdf wants densities in kg/m3. You can either to the ppm to density conversion in the datalogger program, or in the calibration file of ec_ncdf (or even through the gain/offset mechanism of NetCDF, but this is less transparent).

### Sonic temperature
If no thermocouple is present, the sonic temperature is used for the calculations where a temperature is needed. But in order to derive specific humidty from either Krypton or Lymann-alpha data, one needs a temperature. On the other hand one part of the Schotanus et al. correction for the sonic temperature depends on specific humidity. Therefore, a temporary temperature is constructed with both parts of the Schotanus correction applied (where the humidity part is done iteratively: find the correct temperature and specific humidity for the given absolute humidity and sonic temperature). The resulting temperature is used to determine the specific humidity.
The actual humidity part of the Schotanus correction is applied only to the
averaged data, not to the raw data.

### Wind tunnel calibrated sonic
At KNMI sonic anemometers are -sometimes- calibrated in a wind tunnel to determine the directional dependence of the signal. As of version 1.05 of ec_ncdf this can be dealt with. For this purpose a new instrument type, QQType = 6, has been introduced. For this type six extra extra
calibration factors have to be defined in the calibration file (add six lines at the end for QQExt6 to QQExt11).

The method is based on a wind tunnel calibration of the sonic. The real velocity components can be derived from the measured components and the real azimuth and elevation angle. But the latter are not known and have to be determined iteratively from the measured components.
The relationship between the real components and the measured components is:

Ureal = Umeas/(UC1*(1 - 0.5*
        ((Azi + (Elev/0.5236)*UC2)*
        (1 - UC3*Abs(Elev/0.5236)))**2 ))
Vreal = Vmeas*(1 - VC1*Abs(Elev/0.5236))
Wreal = Wmeas/(WC1*(1 - 0.5*(Azi*WC2)**2))
Azi = arctan(V/U)
Elev = arctan(W/sqrt(U**2 + V**2))

where UC1, UC2, UC3, VC1, WC1, WC2 are fitting coefficients (corresponding
to QQExt6, QQExt7, QQExt8, QQExt9, QQExt10 and QQExt11, respectively).
An azimuth angle of zero is supposed to refer to a wind direction from the most optimal direction (i.e. the 'open' side of a sonic). Samples with an absolute azimuth angle of more than 40 degrees are rejected.

### Generic Sonic
In an attempt to make the software more flexible, a generic sonic has been defined, for which the most important coefficients can be set through the calibration file. To this end, five extra calibration coefficients are defined: QQExt5, QQExt6, QQExt7, QQExt8, QQExt9.

#### Side wind correction
One of the instrument dependent corrections is the side-wind correction for the sonic temperature:
Ts = T + (humidity correction) + Au^2 + Bv^2 + Cw^2
where T is the real air temperature, Ts is the sonic temperature, and u, v and w are the instantaneous velocities. In ec_ncdf this correction is applied to the raw samples. The three coefficients A, B, and C are instrument-dependent and can be supplied through the calibration file as QQExt5, QQExt6, QQExt7, respectively. See van Dijk et al, 2004 (internal report 2004/1) on how to compute these factors. In summary: for a symmetric configuration A and B are equal to 0.5*(1+cos2 (alpha)) and C = sin2 (alpha), where alpha is the angle of the sonic path relative to the vertical. For a sonic with orthogonal axes of which one is vertical A, B and C are equal to 2/3.

Note that for a CSAT these factor should be set to zero, since the correction is done internally in the sonic.

#### Coordinate definition
For the coordinate definition, two coefficients are defined:
- QQExt8: defines the handedness of the coordinate system(1 for right handedness like the CSAT, and -1 for left handedness, like the METEK USA-1)
- QQExt9: extra rotation to be done (in degrees); this appeared to be needed for the Kaijo Denkis